## Slide 1: Tool Design

## Slide 2
Data Prep
Download regional StreamCat data files
  ftp://newftp.epa.gov/EPADataCommons/ORD/NHDPlusLandscapeAttributes/StreamCat
Use MergeStreamCatCSVFiles.py to combined files across regions into single StreamCat csv files
Merge CSV Files
Stream Cat
CSV files
Stream Cat
CSV files
Region 03N
Stream Cat
CSV files
Stream Cat
CSV files
Stream Cat
CSV files
Region 05
Stream Cat
CSV files
Stream Cat
CSV files
Stream Cat
CSV files
Region 06
Stream Cat
CSV files
Stream Cat
CSV files
Stream Cat
CSV files
Stream Cat
CSV files
GeoWET\Data\StreamCat\AllRegions\...

## Slide 3
Aq. Species Presences CSV file
Modified
Stream Cat
CSV files
GIS Tool
Extract Species Data & create MaxEnt SWD File
Maxent SWD file
Stream Cat
CSV files
Stream Cat
CSV files
Stream Cat
CSV files
Scenario
Maxent Projection ASCII files
CSV to Maxent ASCII
Current Conditions
Scenario Conditions
1
3
1
Identifies the HUC8s in which the species was found and extracts all StreamCat catchment records within them.
Removes any records with missing data where the species was not found and then any attributes with no data where the species was found.
Removes any attributes with no significant correlation with presence/absence (p > 0.05). Then identifies cross-correlated attributes pairs (r > 0.75) and removes the one with the least correlation with presence/absence.
Formats columns and column names to suit the MaxEnt species with data (SWD) format.
2
Allows user to draw a shape on a map reflecting a change in land cover type.
The user also designates the analysis extent for projecting uplift. This is usually the HUC 6 in which the modification occurs.
Based on this change, adjusts values in appropriate StreamCat attribute values for affected records.
3
Converts each set of StreamCat within the analysis extent (e.g. HUC 6) into its own pseudo-ASCII raster so that it can be used as a MaxEnt projection scenario.
MaxEnt
2
Analysis Extent
Entire state
5
4
4
Listing of each catchment and the estimated percent likelihood of finding the species there based on current conditions (unmodified StreamCat values).
5
Listing of each catchment and the estimated percent likelihood of finding the species there based on altered conditions (modified StreamCat values).
Notes: Aquatic habitat uplift

## Slide 4
Get list of stream cat files that will be affected
Extract stream cat records for HUC 8  dataDF
Update catchment records
  Identify land cover change underneath project
  Decrease values in catchment records of dataDF
Update watershed records
  Identify catchments downstream of project catchment
  Update attribute records
Notes: GIS tool to create a modified SWD file for the HUC8